Re: Engine Management Malfunction Light, ABS, Idle, Roadworthiness

Triumph 800XC
VIN: SMTTRE06B8E622267
Engine: B623616

Over the two days of 22/23 April 2014, I rode my motorcycle for approximately 800km on a variety of terrains. During this time, three problems were encountered.

1. The ABS and Engine Malfunction Light
   I refer to the issue at 01 February 2014 regarding the ABS light and subsequent Engine Malfunction Light. At that time, it was suspected that the front wheel ABS sensor had been temporary blocked, resulting in the ABS light, failure of the ABS and the illumination of the malfunction light. This required an ignition restart for the ABS to restart function.

   After recently, it is apparent that this issue is not a matter of the sensor being temporarily blocked, because it has occurred numerous times and each time, while on rough terrain.

   During the last two days, the ABS light has come on approximately five times, resulting in failure of the ABS system and an ignition restart each time, all while traversing a rough surface terrain.

   Perhaps there is intermittent electrical problem, such as a loose wire, on the ABS system.
2. Failure to idle
   The engine will either not idle at all (with throttle closed) or will idle at an unreasonably low engine speed. This means that when the bike is idling, I must hold the throttle to maintain a running engine.

   I have run the fuel tank dry and used a different fuel. This did not resolve the issue. The engine is otherwise running normally at other throttle positions. There is no power loss from the engine.
3. Red reflector
   The red reflector on the rear mudguard has fallen off. That's because it is held on by two poorly-designed clips.

Sincerely,